## Slide 2
History
Flo Fab was established in 1981 by Denis Gauvreau who created and developed
the products line and constantly being perfected by Marc Gauvreau, as well as by
a team of professional engineers and designers. It’s a combination of existing designs from several renowned products and the innovative ideas of a new generation professionals.
Through the years, Flo Fab has acquired several companies and service entities including : AQUA-PROFAB (ASME Tanks manufacturer), MÉNARD, LÉONARD ÉLECTRIQUE, PMA. , Furthermore Flo Fab purchased equipment, fabrication designs and patterns from IDEALCO, a manufacturer of shell and tube type heat exchangers.
The after sales services, sales, engineering, R&D, production, quality control, accounting and administration departments of all the above companies share the same location.
In December 2014, Marc Gauvreau, son of the founder, acquired all shares of The company. Flo Fab and is constantly investing in new state of the art innovations new product like the XRI series and Prefab Skid for Hydronic Hearing 8 cooling system, pumping systems. This has allowed Flo Fab to retain competent and experienced staff of professionals with varied and specialized abilities that constantly work on improving our existing products and add new engineered solutions that exceeding customer’s expectations .
Flo Fab has grown quite rapidly and now proudly offers of a wide range of products available directly from one manufacturer. This includes pumps & pump packages, tanks, heat exchangers & hydronic accessories. This allows each project stakeholders to enjoy economical savings, peace of mind, best value for their investment and optimized total cost of ownership.

## Slide 3
Flo Fab Pumps
Overview: Design philosophy, common features, etc…
Vertical Inline
  Circulators, closed-coupled, spacer-coupled
Base-mounted
  End suction, closed-coupled, spacer-coupled,
  split case, double-suction, unique configurations
Submersibles
  Sewage, effluent, column, stainless steel, duplex,
  panels, accessories
Flo Fab Pumps

## Slide 4
All pumps are with both casing & impeller wearing rings as standard.
Seals are Viton® with silicon carbide hard faces (NOT Carbon ceramic) for additional heat and chemical resistance.
All seals are rated up to 300ºF as standard.
Standard Motors, Seals, Bearings and couplings.
Heavy industrial class pump casing as it is poured to withstand 300 psi (Flange std.=150psi)
Higher efficiency due to smooth surfaces enhancing fluid mechanics as pump casting molds made from resin pattern NOT wood.
Reliability & Durability
Notes: John Crane Type 21 Mechanical seal !!! Features
The drive band's "dent and groove" design eliminates overstressing of the elastomer bellows to prevent bellows slip and protect the shaft and sleeve from wear.
Non-clogging, single-coil spring provides greater dependability than multiple spring designs and will not foul due to fluid contact.
Flexible elastomer bellows automatically compensates for abnormal shaft-end play, run-out, primary ring wear and equipment tolerances.
Parameters
Temperature Limits-40°F to 400°F/-40°C to 205°C (depending on materials used)
Pressure Limits150 psi(g)/10 bar(g)
Speed LimitsUp to 2500fpm/13m/s, depending on configuration and shaft size

## Slide 5
All Pumps are factory tested with a live 10 sec video and stored on the web quote
Test facilities up to 400 HP with 27,000 gallons test bench with calibrated instruments
Factory designs using Inventor, Revit Files and CAD drawings
Upgraded factory limited warranty 5/8 Years
Quality Control

## Slide 6
Facility Test Bench up to 400Hp

## Slide 7: More than 60% of US projects at the bid phase originate with MASTERSPEC
Proud approved supplier for MASTERSPEC

## Slide 8: Built To Last Rugged Construction…
Cast iron oversized NPT
threaded
conduit box
Leads are fully protected from abrasion
Dual oversized bearings increase life
Stainless steel 50/60HZ nameplate and wiring diagram
Color coded oversized lead AWG
Removable feet for easy F1, F2, F3 conversion. Up to 326T frame
Techtop “Gauntlet”
bearing sealing system
Cast iron inner and outer bearing retainers
Anti-bacterial “Tropicalized” windings
Lap winding eliminates first to last turn contact
Fully phase insulated all
copper windings
Corrosion resistant hardware

## Slide 9: Ingress Protection
The “Gauntlet” – Techtop’s sealing system
Felt seals protect bearing and contain lubricant
Double lip oil seals keep contaminants out and lubrication in.
Slingers keep excess liquid away from seals

## Slide 10: Ingress Protection
How We Handle Condensation
NEW FEATURE: All new motors will be fitted with significantly larger sintered brass drain plugs. The size of the plugs will increase in proportion to the size of the motor.
This allows for more rapid drainage and greatly increases the drain plugs necessary maintenance intervals.
Above: TECHTOP Motor showing one
way drains on both Drive-End-Bell and Opposite- Drive-End Bell.

## Slide 11
Up to 10 distinct curves in the H-Q and P-Q plane programmable into the ISA.
Sensorless
Notes: Instant on-line calculation of power and frequency based on user-defines H-Q reference.

## Slide 12
Easy programming of H-Q and P-Q curves by means of user-friendly download program.
How to do...

## Slide 13: Results...
Pressure on the tested pump can be controlled within +/- 5% of the reference. (Based on lab. tests. Actual accuracy depends on pump and system design).

## Slide 14: Sensorless Pump Control
Advantages
No loose components (sensor, hanging wires,....etc.) One single piece for immediate site installation.
No sensor needed.
Constant pressure or increasing pressure with flow.
Tuning on site not needed.

## Slide 15: The Flo Fab Solution:
Possible STD Limitations Industrial app Not possible

## Slide 16: The Flo Fab Solution:
High precision of pressure ( +/- 5 % ) by means of patent pending motor temperature compensation (Depends on pump and system design).
Stable control by means of 3-point controller with I feed back.
Easy download of pump data via PC programme and serial link.
Flow estimate ( +/- 3 % ).
Setting of pressure on site by means of: Pot meter, 0/4 - 20 mA, 10 V or serial link.
Head at min. and max. flow can be set individually.
PC tools which compress up to 10 sets of pump H-Q-P-n data by means of “Least square fit”.
High efficiency.

## Slide 17: Web capability’s of www.flofab.com
Pump Selections
Expansion Tank Selections
Plate and Frame Heat Exchanger Selections
Hot Water Storage Selections
Make your own quotes
Build a Schedule
www.flofab.com

## Slide 18: Unique XRI Pump Design & Benefits

## Slide 19
XRI Multiple Positions

## Slide 20
https://www.youtube.com/watch?v=WVYCGdltj-o
XRI Pump Video…

## Slide 21
SERIES | 500 | 600 | 840SC | 880RI
SIMILAR TO | Magna / Astro / UP /PL / 00 | 2400 / 1900 / 1600 S / H / 90 / 60 |  | 4300 / 80SC / VLI / KS
TYPE | Circulating Pump | In-Line Circulator | Vertical In-Line Centrifugal Split Coupling | Vertical In-Line Centrifugal Split Coupling
CAPACITIES | up to 234 USGPM (54 m3/hr) | up to 290 USGPM (61 m3/hr) | 454 to 8000 USGPM (1816 m3/hr) | Up to 3000 USGPM (680 m3/hr)
HEAD | up to 43 ft. (14 m) | up to 120 ft. (37 m) | up to 410 ft. (125 m) | up to 650 ft. (198 m)
PRESSURE | up to 145 PSI (999 kPa) | up to 250 PSI (1724 kPa) | up to 600 PSI (4136 kPa) | up to 250 PSI (1724 kPa)
HORSEPOWER | up to 2/5 HP (280 kW) | up to 10 HP (7.5 kW) | up to 400 HP (298 kW) | up to 200 HP (149kW)
DRIVES | ECM Motor ERP Ready | 56C Electric Motors | TC Electric Motors | TC Electric Motors
APPLICATIONS | Water / Glycol | Water / Glycol | Water / Glycol | Water / Glycol
TEMPERATURE | up to 220°F (104°C) | up to 250°F (121°C) | up to 300°F (149°C) | up to 300°F (149 °C)
CONSTRUCTION MATERIAL | Cast Iron, Stainless, Bronze |  | Cast Iron, Bronze Fitted as Standard, Other Materials Also Available | Cast Iron, Bronze Fitted as Standard, Other Materials Also Available
Construction of series XRI
-
VERTICAL IN-LINE PUMPS

## Slide 22
SERIES | 880 | 1000/1004 | 2000 | 2300 / 2600
SIMILAR TO | 80 / VL / 4380 | 1530 / 1532 / CM / C LCS / 4280 | LF / F / 4030 / 1510 / FM | LF / F / 4030 / 1510 / FM
TYPE | Compact In-Line Centrifugal | End Suction, Close Coupled | Radially Split Bearing Frame Pump Mounted With Flexible Coupling Back Pull Out Design | Radially Split Bearing Frame Pump Mounted With Flexible Coupling Back Pull Out Design
CAPACITIES | up to 3000 USGPM (680 m3/hr) | up to 1900 USGPM (431 m3/hr) | up to 1900 USGPM (431 m3/hr) | from 1900 to 6500 USGPM (432 to 1476 m3/hr)
HEAD | up to 650 ft. (198 m) | up to 43 ft. (14 m) | up to 120 ft. (37 m) | up to 410 ft. (125 m)
PRESSURE | up to 250 PSI (1724 kPa) | up to 175 PSI (1206 kPa) | up to 175 PSI (1206 kPa) with 125# flanges | up to 400 PSI (1206 kPa) with 400# flanges
HORSEPOWER | up to 200 HP (149 kW) | up to 200 HP (149 kW) | up to 200 HP (149 kW) | up to 500 HP (373 kW)
DRIVES | JM Electric Motors | JM Electric Motors | T Frame Electric Motors or Diesel Engines | T Frame Electric Motors or Diesel Engines
APPLICATIONS | Water / Glycol | Water / Glycol | Water / Glycol | Water / Glycol
TEMPERATURE | up to 300°F (149 °C) | up to 300°F (149 °C) | up to 300°F (149 °C) | up to 300°F (149 °C)
CONSTRUCTION MATERIAL | Cast Iron, Bronze Fitted as Stan- dard, Other Materials Also Available | Cast Iron, Bronze Fitted as Stan- dard, Other Materials Also Available | Cast Iron, Bronze Fitted as Stan- dard, Other Materials Also Available | Cast Iron, Bronze Fitted as Stan- dard, Other Materials Also Available
SERIES | 4800L | 4800U | 4800/4800H/4900 | 4800V
SIMILAR TO | VSX / TS | VSX | HSC / 4600 / KPGT / HS | KPV
TYPE | Single Stage, Double Suction Split Case | Single Stage, Double Suction Split Case | Horizontally Mounted, Single Stage, Double Suction Split Case | Vertically Mounted, Single Stage, Double Suction Split Case
CAPACITIES | up to 12000 USGPM (2725 m3/hr) | up to 12000 USGPM (2725 m3/hr) | up to 12700 USGPM (2884 m3/hr) | up to 12700 USGPM (2884 m3/hr)
HEAD | up to 750 ft. (227 m) | up to 750 ft. (227 m) | up to 625 ft. (190 m) | up to 625 ft. (190 m)
PRESSURE | up to 600 PSI (4136 kPa) | up to 600 PSI (4136 kPa) | up to 600 PSI (4136 kPa) | up to 600 PSI (4136 kPa)
HORSEPOWER | up to 800 HP (597 kW) | up to 800 HP (597 kW) | up to 1750 HP (1305 kW) | up to 1750 HP (1305 kW)
DRIVES | Electric Motors, Diesel Engines, Steam Turbines | Electric Motors, Diesel Engines, Steam Turbines | Electric Motors, Diesel Engines, Steam Turbines | Electric Motors, Diesel Engines, R.A.G.D
APPLICATIONS | Water / Glycol | Water / Glycol | Water / Glycol | Water / Glycol
TEMPERATURE | up to 300°F (149°C) | up to 300°F (149°C) | up to 300°F (149°C) | up to 300°F (149°C)
CONSTRUCTION MATERIAL | Cast Iron, Bronze Fitted as Standard, Other Materials Also Available | Cast Iron, Bronze Fitted as Standard, Other Materials Also Available | Cast Iron, Bronze Fitted as Standard, Other Materials Also Available | Cast Iron, Bronze Fitted as Standard, Other Materials Also Available
VERTICAL IN-LINE PUMPS + HORIZONTAL BASE MOUNTED + CLOSED COUPLED
SPLIT CASE DOUBLE SUCTION PUMPS

## Slide 23
Flo Fab’s Double Suction Split Case
Series 4800/4800V/4800H/4900
Available in fire
Horizontal
Type: Horizontally Mounted, Single Stage, Double Suction Split Case,
Capacities: up to 12700 USGPM(2884 m3/hr),
Head: up to 625 ft.(190 m),
Pressure: up to 600 PSI (4136 kpa),
Horsepower: up to 1750 HP(1305 KW)
Drives: Electric Motors, Diesel Engines, Steam Turbines
Applications: Water / Glycol
Temperature: up to 300°F (149°C)
Constr. Materials: Cast Iron, Bronze Fitted as Standard, Other
Materials Also Available

## Slide 24
SERIES | PSMCF | PSM | PSF | PST
SIMILAR TO |  | 1535 / 4700 / CR |  | SCX / 1700
TYPE | Vertical Multistage | Vertical Multistage | Flanged Close Coupled Centrifugal | NPT Close Coupled Centrifugal
CAPACITIES | up to 250 USGPM (56 m3/hr) | up to 792 USGPM (180 m3/hr) | 13 to 380 USGPM (3 to 86 m3/hr) | up to 52 USGPM (12m3/hr)
HEAD | up to 930 ft. (283 m) | up to 930 ft. (283 m) | up to 150 ft. (46 m) | up to 150 ft. (46 m)
PRESSURE | up to 430 PSI (2964 kPa) | up to 430 PSI (2964 kPa) | up to 145 PSI (1000 kPa) | up to 115 PSI (793 kPa)
HORSEPOWER | up to 50 HP (37 kW) | up to 100 HP (75 kW) | up to 15 HP (11 kW) | up to 3 HP (2.2 kW)
DRIVES | Vertical Electrical Motor | Vertical Electrical Motor | Electric Close Coupled Motors | Vertical Electrical Motor
APPLICATIONS | Water and Clear Liquids | Water and Clear Liquids | Water and Clear Liquids | Water and Clear Liquids
TEMPERATURE | 5°F(-15°C) to 248°F (120°) | 5°F(-15°C) to 248°F (120°) | up to 225°F (107°C) | up to 225°F (107°C)
CONSTRUCTION MATERIAL | #304 Stainless Steel Optional #316 S/S | Cast Iron as Standard, or Stainless Steel #304 & #316 | #304 Stainless Steel | #304 Stainless Steel
MULTISTAGE, CLOSED COUPLED STAINLESS STEEL PUMPS
SHELL AND TUBE, PLATE AND FRAME, BRAZED TYPE HEAT EXCHANGERS
 | Shell and Tube Heat Exchangers |  | Plate and Frame Heat Exchangers | Brazed Heat Exchangers | 
SERIES | ‘‘W’’ | ‘‘S’’ | ‘‘FFW’’ AHRI | ‘‘BR’’ | IQP1000 / ACH550
TYPE | Water to Water / Glycol to Water | Steam to Water | Steam to Water Water to Water Glycol to Water | Steam to Water Water to Water Glycol to Water | VFD Flo Fab’s Prefered* 200-240V / 3-Phase 380-480V / 3-Phase 500-600V / 3-Phase
CAPACITIES | up to 3000 USGPM 681 m3/hr up to 250 PSI (1724 kpa) Steam |  | up to 10000 USGPM 2271 m3/hr up to 250 PSI (1724 kpa) Steam | up to 400 USGPM 91 m3/hr up to 150 lbs Steam | 150% for 60 sec. (HD), 120% for 60 sec. (ND)
PRESSURE | 150 PSI (1034 kPa) 250 PSI (1724 kPa) |  | 300 PSI (2068 kPa) | 300 PSI (up to 2068 kPa) | 
APPLICATIONS | Water, Glycol or Steam |  | Water, Glycol or Steam | Water, Glycol or Steam | 
TEMPERATURE | up to 300°F (144°C) |  | up to 300°F (144°C) | up to 300°F (144°C) | 
CONSTRUCTION MATERIAL | Carbon Steel or Stainless Steel with Stainless Steel Tubes |  | Carbon Steel, Titanium and Stainless Steel. Other Materials available | Titanium and Stainless Steel. Other Materials available | 

## Slide 25
SERIES | LB-25, 40,75, 215 & 315 | FS-237, 337 & 437, 475, 675, 4110, 6110, 8110 | LBV-40 | LBV-75, 215 & 315 | LBK-75 | LBK-215 & 315
TYPE | Effluent Pump | Multi-Purpose Drainage Pump | Effluent & Sewage Vortex Pump |  | Effluent | Sewage Non Clog Pump
CAPACITIES | up to 175 USGPM (40 m3/hr) | up to 1400 USGPM (317 m3/hr) | up to 159 USGPM (36 m3/hr) |  | up to 185 USGPM (42 m3/hr) | 
HEAD | 8 to 72 ft. (2.4 to 21.5 m) | 10 to 163 ft. (3 to 49 m) | 4 to 59 ft. (1.2 to 18m) |  | 10 to 59 ft. (3 to 18m) | 
PRESSURE | 3/8″ (9 mm) | 3/4″ (19 mm) | 3/4″ (19mm) | 2″ (50mm) | 3/4″ (19mm) | 2″ (50mm)
HORSEPOWER | up to 1 HP (0.75 kW) | up to 30 HP (22 kW) | up to 1 HP (0.75 kW) |  | up to 1 HP (0.75 kW) | 
DRIVES | Air Filled Electrical Motors Explosion Proof | Air Filled Electrical Motors Explosion Proof | Air Filled Electrical Motors Explosion Proof |  | Air Filled Electrical Motors Explosion Proof | 
APPLICATIONS | Water | Water | Water, Sewage & Waste Liquids |  | Water | Water & Waste Liquids
TEMPERATURE | up to 200°F (94 °C) | up to 200°F (94 °C) | up to 200°F (94 °C) |  | up to 200°F (94 °C) | 
CONSTRUCTION MATERIALS | Cast Iron | Cast Iron and Stainless Steel | Cast Iron |  | Cast Iron | 
PLUMBING
SERIES | FBV-332 | FBV-337 & 437 | FGC-015 / FGC-022 | BAF | Sub Accessories
 |  |  | FGC-037 / FGC-055 |  | 
TYPE | Sewage Non Clog Pump |  | Sewage Grinder Pump | Break Away Fitting | 
CAPACITIES | up to 317 USGPM 72 m3/hr |  | up to 61 USGPM 14 m3/hr |  | 
HEAD | 8 to 66ft (2.4 to 20 m) |  | 17 to 105ft (5.2 to 32 m) |  | 
PRESSURE | 2″ (50 mm) | 3″ (80 mm) | 3/4″ (19 mm) |  | 
HORSEPOWER | up to 5 HP (3.7 kW) |  | up to 5 HP (3.7 kW) |  | 
DRIVES | Air Filled Electrical Motors Explosion Proof |  | Air Filled Electrical Motor Explosion Proof |  | 
APPLICATIONS | Water, Sewage & Waste Liquids |  | Water, Sewage & Waste Liquids |  | 
TEMPERATURE | up to 200°F (94°C) |  | up to 200°F (94°C) |  | 
CONSTRUCTION MATERIAL | Cast Iron |  | Cast Iron | Cast Iron | 
SUBMERSIBLE PUMPS

## Slide 26
ASME TANKS & AIR SEPARATORS
SERIES | SEP | ADSR/AD | RDT/BT | RLU / RWU | RSE
SIMILAR TO | RL | 4900 | RDT: AX / OT / NTA / CAX / D BT: AL / NLA / CA / B / ST-DHW |  | 
TYPE | Vortex - Tangential Air Separator (With or Without Strainer) | In-Line Air/Dirt Sepa- rator (With Strainer) | Non Replaceable Bladder Expansion Tank | Hot Water Storage Tank with Heater | Hot Water Storage Tank
 |  |  | Replaceable Bladder Exp. Tank (with bottom system connection) |  | 
CAPACITIES | 56 to 67000 USGPM (13 to 15217 m3/hr) | 69 to 12100 USGPM (16 to 2748 m3/hr) | 3 to 3962 Gallons (11 to 15000 liters) | 100 to 15000 Gallons (379 to 56781 liters) | 
CONNECTIONS | 2″ to 36″ Diameter (50 mm to 914 mm) | 2″ to 36″ Diameter (50 mm to 914 mm) | 1″ to 3″ 25 mm to 75 mm | As Requested | 
PRESSURE | up to 250PSI (1724 kPa) | up to 250PSI (1724 kPa) | up to 250PSI (1724 kPa) | up to 250PSI (1724 kPa) | 
TEMPERATURE | up to 550°F (288°C) | up to 550°F (288°C) | up to 240°F (115°C) | up to 550°F (288°C) | 
CONSTRUCTION MATERIAL | Carbon Steel or Stainless Steel | Carbon Steel or Stainless Steel | Carbon Steel EPDM | Carbon Steel or Stainless Steel | 
  Heating and Cooling Systems
  Module HC will be composed of two pumps, control panel VFD, expansion tank, air separator, chemical pot Feeder, and glycol fill sys- tem (optional), balancing valves, isolation valves, air vents and drain connections, multifunction valves, suction diffusers or Y strainers, interconnecting black steel schedule 40 piping. All package compo- nents are mounted on a structural steel base with lifting lugs.
.

## Slide 27
9
HYDRONIC ACCESSORIES
AIR VENT - MV
Material: Cast Iron
Pressure: MV15 150 PSIG at 345°F
MV15 300 PSIG at 400°F
Size Range : 3/4″
Connections : Threaded
AIR VENT - AA
Material: Brass
Pressure: 150 PSIG at 200°F Size Range : 1/8″ and 1/4″ Connections : Threaded
BUTTERFLY VALVE - BFVZ - L
Material: Cast Iron Body, Stainless Steel
Disc, EPDM Seat Pressure : 175 PSIG at 225°F up to 12″
150 PSIG at 250°F
from 14″ to 24″ Size Range : 2″ to 24″ Body Style : Lug
MULTIFUNCTION VALVE - MFV
Material: Ductile Iron and Stainless Steel Disc Pressure: 150 PSIG at 225°F
Size Range : 2″ to 18″
Connections: MFV-F: Flanged
PRESSURE AND OR TEMPERATURE PORTS
Material : Bronze
Pressure : 1000 PSIG at 140°F
Size Range : 1/4″
Connections: SS2501 :Threaded
SS2511 : Threaded Extended
WAFER CHECK VALVE - LSDDB
Material: Cast Iron Body, Stainless Steel
Disc, EPDM Seat Pressure: 175 PSIG at 225°F up to 12″
150 PSIG at 250°F
from 14″ to 24″ Size Range : 2″ to 24″ Body Style : Wafer
SUCTION DIFFUSER - ASDFF
Material: Cast Iron Body, Stainless Steel Sceen Pressure: 175 PSIG at 250°F with water
200 PSIG at 150°F with steem
Size Range : 2″ to 20″
Connections : Flanged
2000 - FIXED BLADDER EXPANSION TANK
Capacities: 2 to 132 Gallons (8 to 528 liters) Pressure: up to 150PSI (1034kpa) Temperature : up to 200°F (93°C)
Materials: Carbon Steel, Butyl
FLEXIBLE - ST
Material: Steel and Stainless Steel Pressure : 475 PSIG at 850°F with water Size Range : 1/2″ to 2″
Connections: Threaded
UNION ARCH FLEXIBLE - DUT
Material : Steel Union and EPDM
Pressure : 214 PSIG at 250°F with water
Size Range : 1/2″ to 12″
Connections: Threaded Double
SINGLE ARCH FLEXIBLE - SSP & DSP
Material: Steel Flanged and EPDM Pressure: 214 PSIG at 240°F with water Size Range : 1 1/2″ to 14″
Connections: SSP Flanged Single
DSP Flanged Double
STANDARD FLANGED CONNECTOR - SM
Material: Steel and Stainless Steel Pressure: 125 PSIG at 450°F wih water Size Range : 2″ to 16″
Body Style : Flanged

## Slide 28
Quotation Requirements for Skid Package
What we need ?
1.1 System PID
1.2 Pumps, Tanks and Heat Exchangers Schedule
1.3 Cut sheets for non Flo Fab parts like
ex. Boilers, Chillers, etc...
1.4 Skids footprint
1.5 Mechanical room footprint
1.6 Details sequence of control
Quality Control
All pumps are factory tested and certified performance
test is available when requested by the consultant.
Test facilities up to 400 HP with 27,000 gallon test
bench with calibrated instruments...
2.1 Heating and Cooling Systems
2.2 Module HC will be composed of two pumps, control panel VFD, expansion tank, air separator, chemical pot Feeder, and glycol fill system (optional), balancing valves, isolation valves, air vents and drain connections, multifunction valves, suction diffusers or Y strainers, interconnecting black steel schedule 40 piping. All package components are mounted on a structural steel base with lifting lugs....

## Slide 29
https://youtu.be/rEgjRUsB8jM Miami Hospital
https://youtu.be/1pRTIxS817g Shop
https://youtu.be/ZNccm-E3Ras Skid Lifting
Explanation Videos…

## Slide 33: .

## Slide 34
- Solution for both : New construction and Retrofit.
- Easily add more modules for future expansion.
- One single point of Responsibility / Contact .
- One single submittal for approval Vs. Individual submittals for each component.
- Financial : Cost reduction, Effectively reduce total cost of ownership for all project stake holders (Contractor / Consultant Engineer / End User)
- Financial : Space saving due to optimized space utilization.
- Financial : Time (Cost) saving : Skid built in parallel during building construction, also .
- Financial : : Cash flow management: One single invoice / payment for all works
- Financial :: Overhead saving including project management, logistical
coordination, insurance expense, ...etc.
- Financial : No surplus or extra components left after
fabrication by contractor.
- Time (Cost) saving : No construction delay due to
missing one single component order, wrong delivery
or defective component.
- Quality: Assembly within controlled environment by
certified technicians / welders using approved work
methods / procedures.
- Quality / Financial : Factory wired and tested = site
plug & play
- Safety: Avoid unpleasant site safety incidents and
lost days as we tremendously minimize job site
man-hours.
Skid Advantages

## Slide 35: Modularized Packaged Chilling System
Produced within Controlled Environment :
    Manufactured, Not Constructed
    Proven Engineered Design and Fabrication Standards
    Strict Quality Control
    Controlled Environment with High Safety Standards
    Established Knowledgeable Skilled Workforce
    Job Site Progress / Conditions Irrelevant to Production
Notes: 35

## Slide 36: Multiple Chillers

## Slide 37: Maintenance Enhancements : Chiller Tube Service Access
Notes: 37

## Slide 38: Overhead Gantry and Chain Pulley Block
Maintenance Enhancements : Pump removal Design
Notes: 38

## Slide 39
How it look like in the field inside the building ?

## Slide 40
High Profile Jobs

## Slide 42
How it look like inside a shelter ?

## Slide 43
* How it look in the field outside the building.
How it look like in the field outside the building ?

## Slide 44
CHI
Chiller
Package
BOI
Boiler
Package
D-CPS-HT Duplex
Constant Pressure
System
Packaged
Systems

## Slide 45
HCE Heating
Cooling with Enclosure
LCOO Large Cooling Package
Packaged
Systems

## Slide 46: Enclosures

## Slide 47: Video: https://mail.google.com/mail/u/0/#inbox?projector=1

## Slide 48
Industry leading – 25-year Warranty
Exclusive FiberBeam™ and
FiberWrap ™ Technology
Built to highest standards
Superior responsiveness and attention
to detail in all phases of a project.

## Slide 49: Enclosure installation on skid package

## Slide 50: Complete assembly with Shelter Works enclosure

## Slide 51: How to rig equipment

## Slide 52: Special package delivery

## Slide 56: World trade center Nyc

## Slide 58: Modular packaged Chilling Systems - Solutions to Suit Every Application
Apartment units
Homes
High-rise Apartments
Lodging
Retail
Medical Clinics
Schools
Shopping Malls
Small Commercial
Colleges & Universities
Government
Large Commercial
High Technology
Airports
Hospitals
Life Sciences
Arenas/Convention Centers
Residential Mid Market Complex

## Slide 59: OTHERS !!!!!! Middle East Project List (Sep 2012)
# | Year | Project / Client | Application | Type of Plant | Country | Qty | Total Tons | Voltage
1 | 2005 | Empower-1 | District Cooling | Mobile Temporary Plant | UAE | 7 | 12,300 | 3300 / 400
2 | 2005 | Tabreed | District Cooling | Mobile Temporary Plant | Bahrain | 2 | 2,400 | 400
3 | 2005 | Dubai Festival City | District Cooling | Permanent Plant | UAE | 10 | 50,000 | 11000 / 400
4 | 2006 | Dubai Investment Park | District Cooling | Permanent Plant + ETS | UAE | 3 | 12,000 | 11000 / 400
5 | 2006 | Deira City Centre | Shopping Mall | Replacement Permanent Plant | UAE | 2 | 2,600 | 11000 / 400
6 | 2007 | Dubai World Trade Centre | Residential Bldgs | Mobile Temporary Plant | UAE | 2 | 2,400 | 11000 / 400
7 | 2007 | Empower-2 | District Cooling | Mobile Temporary Plant | UAE | 8 | 20,000 | 11000 / 400
8 | 2007 | Emicool | District Cooling | Mobile Temporary Plant | UAE | 4 | 4,800 | 11000 / 400
9 | 2008 | Al Naboodah | Villa Complex | Permanent Plant (Screw Chlrs) | UAE | 1 | 1,200 | 400
10 | 2008 | Empower-3 | District Cooling | Mobile Temporary Plant | UAE | 9 | 22,000 | 3300 / 400
11 | 2008 | Empower-4 | District Cooling | Mobile Temporary Plant | UAE | 1 | 2,000 | 3300 / 400
12 | 2008 | Al Naboodah Extension | Office Bldg | Permanent Plant (Screw Chlr) | UAE | 1 | 400 | 400
13 | 2009 | Dubai World Trade Centre | Exhibition Hall | Long Term Temporary Plant | UAE | 2 | 4,000 | 11000 / 400
14 | 2009 | Saudi ARAMCO | Office Bldg | Permanent Plant | Saudi | 1 | 4,000 | 4160 / 460
15 | 2010 | Al Rayyana / Sorouh | Residential Bldgs | Permanent Plant | UAE | 1 | 7,200 | 11000 / 400
16 | 2011 | Malaiha Camp / Tabreed | Military Camp | Permanent Plant | UAE | 2 | 10,000 | 11/3.3kV/400
17 | 2011 | Capitala Rihan Heights | Residential Bldgs | Permanent Plant | UAE | 1 | 4,000 | 11000 / 400
18 | 2011 | Sh. Zayed University | University Campus | Permanent Plant | UAE | 2 | 9,450 | 11000 / 400
19 | 2011 | GASCO (OilCo) | Indl. Refrigeration | Replacement Permanent Plant | UAE | 1 | 1,300 | 3300 / 400
20 | 2012 | Empower-5 | District Cooling | Mobile Temporary Plant | UAE | 8 | 20,000 | 11000 / 400
21 | 2012 | Emirates Hangars | Hangar Cooling | Permanent Plant | UAE | 1 | 3,080 | 400
 |  |  |  |  | Total | 69 | 195,130 | 
The Gazette
Montréal, QC, CA
Regional Medical Center
Muskogee, OK, USA
Research and Medical Clinic
Tulsa, OK, USA

## Slide 60
More Jobs
Canadian National
Montreal QC, CA
Montreal’s Archives
Montreal, QC, CA
The Gazette
Montréal, QC, CA
Wawanesa
Mont-Royal, QC, CA
Muskogee Regional
Medical Center
Muskogee, OK, USA
Research and Medical Clinic
Tulsa, OK, USA

## Slide 61
More Jobs

## Slide 63
Thank You for
Your participation!
Visit our Website
www.flofab.com