## Slide 2: Sensorless Pump Control
Product
  Open-loop control of differential pressure (head) without a pressure feedback
  Constant or proportional head control optional
  Simple flow-meter functionality

## Slide 3
Controller structure based on internal power measurement
How to do...

## Slide 4
Up to 10 distinct curves in the H-Q and P-Q plane programmable into the ISA.
How to do...
Notes: Instant on-line calculation of power and frequency based on user-defines H-Q reference.

## Slide 5
Easy programming of H-Q and P-Q curves by means of user-friendly download program.
How to do...

## Slide 6: Results...
Pressure on the tested pump can be controlled within +/- 5% of the reference. (Based on lab. tests. Actual accuracy depends on pump and system design).

## Slide 7: Sensorless Pump Control
Advantages
No loose components (sensor, hanging wires,....etc.) One single piece for immediate site installation.
No sensor needed.
Constant pressure or increasing pressure with flow.
Tuning on site not needed.

## Slide 8: The Flo Fab Solution:
Possible Limitations Not possible

## Slide 9: The Flo Fab Solution:
High precision of pressure ( +/- 5 % ) by means of patent pending motor temperature compensation (Depends on pump and system design).
Stable control by means of 3-point controller with I feed back.
Easy download of pump data via PC programme and serial link.
Flow estimate ( +/- 3 % ).
Setting of pressure on site by means of: Pot meter, 0/4 - 20 mA, 10 V or serial link.
Head at min. and max. flow can be set individually.
PC tools which compress up to 10 sets of pump H-Q-P-n data by means of “Least square fit”.
High efficiency.